## Slide 1
SECURITY COMPLIANCE
vSphere Security Compliance Guide
Hardening Audit Summary - executive overview of checks against the VMware Security Config…
Generated: 2026-09-10 17:19
Objects assessed: 66
Baseline: VMware vSphere Security Configuration Guide
TOTAL CHECKS
2304
PASS
1401
60.8%
FAIL
643
INFO
260
P0 CRITICAL GAPS
217
EXECUTIVE SUMMARY
Across 66 assessed object(s), 1401 of 2304 checks passed (60.8%). 217 finding(s) are rated P0 (critical priority) and should be remediated before the next audit cycle; 132 are P1.
Pass Rate by Object Type
ESXi (10 object(s))
67%
VM (56 object(s))
57%
Source: Output_20260908_220829 | Generated 2026-09-10 17:19
1 / 9

## Slide 2
Compliance Overview
Pass rate by object and open-finding priority mix
Chart: 
Open Findings by Priority
Priority | Fail Count
P0 | 217
P1 | 132
P2 | 52
Advanced | 126
P0 items represent the highest-risk configuration gaps and should be remediated first; see the priority findings and remediation pages that follow.
OBSERVATION
The lowest pass rate is 0% on VM: epa-harbor (6 failed check(s)). Review this object first when planning remediation work.
Source: Output_20260908_220829 | Generated 2026-09-10 17:19
2 / 9

## Slide 3
Priority Findings (Failed Controls)
Sorted by remediation priority - P0 first (1/5)
SCG ID | Title | Priority | Type | Object | Baseline
esxi-8.account-password-policies | The ESXI host must enforce password com… | P0 | ESXi | fu-01.***.*** | "similar=deny r…
esxi-8.vib-trusted-binaries | Only run binaries delivered via signed… | P0 | ESXi | fu-01.***.*** | True
esxi-8.memeagerzero | The ESXi host must enable volatile key… | P0 | ESXi | fu-01.***.*** | 1
esxi-8.logs-audit-local | The ESXi host must enable audit record… | P0 | ESXi | fu-01.***.*** | TRUE
esxi-8.logs-remote-tls-x509 | The ESXi host must use strict x509 veri… | P0 | ESXi | fu-01.***.*** | TRUE
esxi-8.account-dcui | The ESXi host must deny shell access fo… | P0 | ESXi | fu-01.***.*** | false
esxi-8.secureboot | The ESXi host must enable Secure Boot. | P0 | ESXi | fu-01.***.*** | True
esxi-8.secureboot-enforcement | The ESXi host must enable TPM-based Sec… | P0 | ESXi | fu-01.***.*** | True
esxi-8.tls-profile | The ESXi host must maintain confidentia… | P0 | ESXi | fu-01.***.*** | NIST_2024
esxi-8.deactivate-cim | The ESXi CIM service should be deactiva… | P0 | ESXi | fu-01.***.*** | Stopped, Start…
esxi-8.deactivate-snmp | The ESXi SNMP service should be deactiv… | P0 | ESXi | fu-01.***.*** | Stopped, Start…
esxi-8.lockdown-mode | Enable normal lockdown mode on the ESXi… | P0 | ESXi | fu-01.***.*** | lockdownNormal
esxi-8.lockdown-mode | Enable normal lockdown mode on the ESXi… | P0 | ESXi | fu-01.***.*** | lockdownNormal
esxi-8.account-password-policies | The ESXI host must enforce password com… | P0 | ESXi | fu-02.***.*** | "similar=deny r…
Source: Output_20260908_220829 | Generated 2026-09-10 17:19
3 / 9

## Slide 4
Priority Findings (Failed Controls)
Sorted by remediation priority - P0 first (2/5)
SCG ID | Title | Priority | Type | Object | Baseline
esxi-8.vib-trusted-binaries | Only run binaries delivered via signed… | P0 | ESXi | fu-02.***.*** | True
esxi-8.memeagerzero | The ESXi host must enable volatile key… | P0 | ESXi | fu-02.***.*** | 1
esxi-8.logs-audit-local | The ESXi host must enable audit record… | P0 | ESXi | fu-02.***.*** | TRUE
esxi-8.logs-remote-tls-x509 | The ESXi host must use strict x509 veri… | P0 | ESXi | fu-02.***.*** | TRUE
esxi-8.account-dcui | The ESXi host must deny shell access fo… | P0 | ESXi | fu-02.***.*** | false
esxi-8.secureboot | The ESXi host must enable Secure Boot. | P0 | ESXi | fu-02.***.*** | True
esxi-8.secureboot-enforcement | The ESXi host must enable TPM-based Sec… | P0 | ESXi | fu-02.***.*** | True
esxi-8.tls-profile | The ESXi host must maintain confidentia… | P0 | ESXi | fu-02.***.*** | NIST_2024
esxi-8.deactivate-cim | The ESXi CIM service should be deactiva… | P0 | ESXi | fu-02.***.*** | Stopped, Start…
esxi-8.deactivate-snmp | The ESXi SNMP service should be deactiv… | P0 | ESXi | fu-02.***.*** | Stopped, Start…
esxi-8.lockdown-mode | Enable normal lockdown mode on the ESXi… | P0 | ESXi | fu-02.***.*** | lockdownNormal
esxi-8.lockdown-mode | Enable normal lockdown mode on the ESXi… | P0 | ESXi | fu-02.***.*** | lockdownNormal
esxi-8.account-password-policies | The ESXI host must enforce password com… | P0 | ESXi | fu-03.***.*** | "similar=deny r…
esxi-8.vib-trusted-binaries | Only run binaries delivered via signed… | P0 | ESXi | fu-03.***.*** | True
Source: Output_20260908_220829 | Generated 2026-09-10 17:19
4 / 9

## Slide 5
Priority Findings (Failed Controls)
Sorted by remediation priority - P0 first (3/5)
SCG ID | Title | Priority | Type | Object | Baseline
esxi-8.memeagerzero | The ESXi host must enable volatile key… | P0 | ESXi | fu-03.***.*** | 1
esxi-8.logs-audit-local | The ESXi host must enable audit record… | P0 | ESXi | fu-03.***.*** | TRUE
esxi-8.logs-remote-tls-x509 | The ESXi host must use strict x509 veri… | P0 | ESXi | fu-03.***.*** | TRUE
esxi-8.account-dcui | The ESXi host must deny shell access fo… | P0 | ESXi | fu-03.***.*** | false
esxi-8.secureboot | The ESXi host must enable Secure Boot. | P0 | ESXi | fu-03.***.*** | True
esxi-8.secureboot-enforcement | The ESXi host must enable TPM-based Sec… | P0 | ESXi | fu-03.***.*** | True
esxi-8.tls-profile | The ESXi host must maintain confidentia… | P0 | ESXi | fu-03.***.*** | NIST_2024
esxi-8.deactivate-cim | The ESXi CIM service should be deactiva… | P0 | ESXi | fu-03.***.*** | Stopped, Start…
esxi-8.deactivate-snmp | The ESXi SNMP service should be deactiv… | P0 | ESXi | fu-03.***.*** | Stopped, Start…
esxi-8.lockdown-mode | Enable normal lockdown mode on the ESXi… | P0 | ESXi | fu-03.***.*** | lockdownNormal
esxi-8.lockdown-mode | Enable normal lockdown mode on the ESXi… | P0 | ESXi | fu-03.***.*** | lockdownNormal
esxi-8.account-password-policies | The ESXI host must enforce password com… | P0 | ESXi | fu-04.***.*** | "similar=deny r…
esxi-8.vib-trusted-binaries | Only run binaries delivered via signed… | P0 | ESXi | fu-04.***.*** | True
esxi-8.logs-audit-remote | The ESXi host must transmit audit recor… | P0 | ESXi | fu-04.***.*** | TRUE
Source: Output_20260908_220829 | Generated 2026-09-10 17:19
5 / 9

## Slide 6
Priority Findings (Failed Controls)
Sorted by remediation priority - P0 first (4/5)
SCG ID | Title | Priority | Type | Object | Baseline
esxi-8.memeagerzero | The ESXi host must enable volatile key… | P0 | ESXi | fu-04.***.*** | 1
esxi-8.logs-audit-local | The ESXi host must enable audit record… | P0 | ESXi | fu-04.***.*** | TRUE
esxi-8.logs-remote-tls-x509 | The ESXi host must use strict x509 veri… | P0 | ESXi | fu-04.***.*** | TRUE
esxi-8.logs-remote | Configure a remote log server for the E… | P0 | ESXi | fu-04.***.*** | Site-Specific L…
esxi-8.account-dcui | The ESXi host must deny shell access fo… | P0 | ESXi | fu-04.***.*** | false
esxi-8.secureboot | The ESXi host must enable Secure Boot. | P0 | ESXi | fu-04.***.*** | True
esxi-8.secureboot-enforcement | The ESXi host must enable TPM-based Sec… | P0 | ESXi | fu-04.***.*** | True
esxi-8.tls-profile | The ESXi host must maintain confidentia… | P0 | ESXi | fu-04.***.*** | NIST_2024
esxi-8.deactivate-cim | The ESXi CIM service should be deactiva… | P0 | ESXi | fu-04.***.*** | Stopped, Start…
esxi-8.deactivate-snmp | The ESXi SNMP service should be deactiv… | P0 | ESXi | fu-04.***.*** | Stopped, Start…
esxi-8.lockdown-mode | Enable normal lockdown mode on the ESXi… | P0 | ESXi | fu-04.***.*** | lockdownNormal
esxi-8.lockdown-mode | Enable normal lockdown mode on the ESXi… | P0 | ESXi | fu-04.***.*** | lockdownNormal
esxi-8.account-password-policies | The ESXI host must enforce password com… | P0 | ESXi | fu-05.***.*** | "similar=deny r…
esxi-8.vib-trusted-binaries | Only run binaries delivered via signed… | P0 | ESXi | fu-05.***.*** | True
Source: Output_20260908_220829 | Generated 2026-09-10 17:19
6 / 9

## Slide 7
Priority Findings (Failed Controls)
Sorted by remediation priority - P0 first (5/5)
SCG ID | Title | Priority | Type | Object | Baseline
esxi-8.logs-audit-remote | The ESXi host must transmit audit recor… | P0 | ESXi | fu-05.***.*** | TRUE
esxi-8.memeagerzero | The ESXi host must enable volatile key… | P0 | ESXi | fu-05.***.*** | 1
esxi-8.logs-audit-local | The ESXi host must enable audit record… | P0 | ESXi | fu-05.***.*** | TRUE
esxi-8.logs-remote-tls-x509 | The ESXi host must use strict x509 veri… | P0 | ESXi | fu-05.***.*** | TRUE
Source: Output_20260908_220829 | Generated 2026-09-10 17:19
7 / 9

## Slide 8
Remediation Highlights
Distinct P0 (critical priority) findings and suggested remediation
esxi-8.account-password-policies - The ESXI host must enforce passwo…
• Affected: 5 object(s), e.g. ESXi / fu-01.***.***
• Finding: fu-01.***.***: Security.PasswordQualityControl not configured correctly (retry=…
• Remediation: Get-VMHost -Name $ESXi | Get-AdvancedSetting Security.PasswordQualityControl | Set-Advanc…
• DISA STIG: ESXI-80-000035 ESXI-80-000044
• PCI DSS 4.0: 8.3.1 8.3.6
esxi-8.vib-trusted-binaries - Only run binaries delivered via s…
• Affected: 5 object(s), e.g. ESXi / fu-01.***.***
• Finding: fu-01.***.***: VMkernel.Boot.execInstalledOnly not configured correctly (False)
• Remediation: Get-VMHost -Name $ESXi | Get-AdvancedSetting VMkernel.Boot.execInstalledOnly | Set-Advanc…
• DISA STIG: ESXI-80-000244
• PCI DSS 4.0: 5.2.3
esxi-8.memeagerzero - The ESXi host must enable volatil…
• Affected: 5 object(s), e.g. ESXi / fu-01.***.***
• Finding: fu-01.***.***: Mem.MemEagerZero not configured correctly (0)
• Remediation: Get-VMHost -Name $ESXi | Get-AdvancedSetting Mem.MemEagerZero | Set-AdvancedSetting -Valu…
• DISA STIG: ESXI-80-000225
• PCI DSS 4.0: 3.6.1
COVERAGE NOTE
60 P0 finding(s) span 14 distinct control(s). 11 additional P0 control(s) are not shown here - see the Priority Findings pages for the full list.
Source: Output_20260908_220829 | Generated 2026-09-10 17:19
8 / 9

## Slide 9
Recommendations & Next Steps
1) Remediate P0 Gaps
• 217 critical (P0) findings require immediate remediation.
• Assign owners per object type (vCenter / ESXi / VM) and track to closure.
2) Schedule P1/P2
• 132 P1 and 52 P2 findings can follow in the next maintenance window.
• Group by SCG ID to batch similar fixes across objects.
3) Re-Baseline
• Current overall pass rate is 60.8%.
• Re-run the hardening audit after remediation to confirm improvement and refresh this report.
NEXT STEPS
This summary was generated from Output_20260908_220829. Track remediation progress by comparing it against the results produced the next time menu [3] (vCenter Security Suite) is run (66 object(s) assessed, overall pass rate 60.8%).
Source: Output_20260908_220829 | Generated 2026-09-10 17:19
9 / 9